## Slide 1: Signals Signal : Signal is a function, that represents the variation of a physical quantity with respect to any parameter.
EXAMPLES :
Motion: The motion of an object can be considered to be a signal.
Sound : sound is a vibration of a medium (such as air).
Image : A picture or image consists of a brightness or color signal.
Video :A video signal is a sequence of images

## Slide 2
Analog Signal: Analog signal is a signal which can take any value within the given limit
Discrete Time Signal: The signal which is defined for discrete intervals of time is called discrete time signal

## Slide 3
Why Digital Electronics?
All real life signals are analog in nature and at first sight, it seems use of analog is much better as compared to digital signal. But digital signals have various advantages over the analog signal like noise immunity. Digital signal is used in communication process to minimize the effect of noise
Digital Signals carry more information per unit time as compared to analog signals
Quality of digital signal is better over long distance transmission
We can encrypt digital signals
Noise removal is easy in digital signals

## Slide 4
Important points:
We use analog to digital converter to convert analog signal to digital signal
Computer, calculator, digital watch, measuring instruments are some examples of digital system
We use digital to analog converter to convert digital signal back to analog signal
0V is represented by ''0​​.
5V is represented by ''1.
We can represent two levels by using one switch.
If switch is open it is OFF(0) and
if switch is closed it is ON(1) .
If n is number of levels and m is number of switches, then n=2​​ power​ m.

## Slide 5: Chapter - I Number System
5

## Slide 6: Chapter I – Number System
Introduction to digital signal, Advantages of Digital System over analog systems
  Number Systems: Different types of number systems( Binary,
Octal, Hexadecimal ), conversion of number systems,
  Binary arithmetic: Addition, Subtraction, Multiplication, Division.
  Subtraction using 1’s complement and 2’s complement
Codes
  Codes -BCD, Gray Code, Excess-3, ASCII code
  BCD addition, BCD subtraction using 9’s and 10’ complement
(Numericals based on above topic).

## Slide 7: Chapter I – Number System
Introduction to digital signal, Advantages of Digital System over analog systems

## Slide 8: Number System
A number system defines a set of values used to represent quantity.

## Slide 9: Different Number Systems
Decimal Number System
  Base 10
Binary Number System
  Base 2
Octal Number System
  Base 8
Hexadecimal Number System
      -Base 16

## Slide 10: Decimal Number System
Decimal number system contains ten unique symbols 0,1,2,3,4,5,6,7,8 and 9
Since counting in decimal involves ten symbols, we can say that its base or radix is ten.
It is a positional weighted system

## Slide 11: Decimal Number System
Structure:
Decimal No.
Positional Weights
....
Decimal Point
MSD
LSD
...... d3
d 2 d1 d 0 . d  1 d  2
100
101
103 102
101
102

## Slide 12
Binary Number System
Binary number system is a positional weighted system
It contains two unique symbols 0 and 1
Since counting in binary involves two symbols, we can say that its base or radix is two.

## Slide 13: Binary Number System
A binary digit is called a “Bit”
A binary number consists of a sequence of bits, each of which is either a 0 or a 1.
The binary point separates the integer and fraction parts

## Slide 14: Structure:
Binary Number System
Binary No.
Positional Weights
....
Binary Point
MSB
LSB
...... b3
b2 b1 b0 . b  1 b  2
20
21
23 22
21 22

## Slide 15: Binary Number System
Decimal No. | Binary No.
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
Decimal No. | Binary No.
8 | 1000
9 | 1001
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111

## Slide 16: Octal Number System
Octal number system is a positional weighted system
It contains eight unique symbols 0,1,2,3,4,5,6 and 7
Since counting in octal involves eight symbols, we can say that its base or radix is eight.
The largest value of a digit in the octal system will be 7.

## Slide 17: Structure:
Octal Number System
Octal No.
Positional Weights
Radix Point
MSD
LSD
...... O3
O  2 ....
O2 O1 O0 . O  1
83 82 81 80
81 82

## Slide 18: Octal Number System
8/29/2017
Amit Nevase
30
Decimal No. | Binary No. | Octal No.
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 10
9 | 1001 | 11
10 | 1010 | 12
11 | 1011 | 13
12 | 1100 | 14
13 | 1101 | 15

## Slide 19
Hexadecimal Number System (HEX)
Binary numbers are long. These numbers are fine for machines but are too lengthy to be handled by human beings. So there is a need to represent the binary numbers concisely.
One number system developed with this objective is the hexadecimal number system (or Hex)

## Slide 20: Hexadecimal Number System (HEX)
Hex number system is a positional weighted system
It contains sixteen unique symbols 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E and F.
Since counting in hex involves sixteen symbols, we can say that its base or radix is sixteen.

## Slide 21
Hexadecimal Number System (HEX)
Structure:
Hex No.
Positional Weights
....
Radix Point
MSD
LSD
H2 H1
...... H3
. H  1 H  2
H 0
163 162 161 160
161
162

## Slide 22: Hexadecimal Number System (HEX)
Decimal No. | Binary No. | Hex No.
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
Decimal No. | Binary No. | Hex No.
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 23: Conversion Among Bases
Hexadecimal
Decimal
Octal
Binary
Possibilities

## Slide 24: Conversion from Decimal Number to Binary Number
Hexadecimal
Decimal
Octal
Binary

## Slide 25: Conversion of Decimal number into Binary number (Integer Number)
Procedure:
Divide the decimal no by the base 2, noting the remainder.
Continue to divide the quotient by 2 until there is nothing left, keeping the track of the remainders from each step.
List the remainder values in reverse order to
d the number’s biAnmitaNervayse equivalent

## Slide 26: Example: Convert 105 decimal number in to it’s equivalent binary number.

## Slide 27: Example: Convert 105 decimal number in to it’s equivalent binary number.
105
2

## Slide 28: Example: Convert 105 decimal number in to it’s equivalent binary number.
2 | 105
2 | 52
1

## Slide 29: Example: Convert 105 decimal number in to it’s equivalent binary number.
2 | 105
2 | 52
2 | 26
1
0

## Slide 30: Example: Convert 105 decimal number in to it’s equivalent binary number.
2 | 105
2 | 52
2 | 26
2 | 13
1
0
0

## Slide 31: Example: Convert 105 decimal number in to it’s equivalent binary number.
2 | 105
2 | 52
2 | 26
2 | 13
2 | 6
1
0
0
1

## Slide 32: Example: Convert 105 decimal number in to it’s equivalent binary number.
2 | 105
2 | 52
2 | 26
2 | 13
2 | 6
2 | 3
1
0
0
1
0

## Slide 33: Example: Convert 105 decimal number in to it’s equivalent binary number.
2 | 105
2 | 52
2 | 26
2 | 13
2 | 6
2 | 3
2 | 1
1
0
0
1
0
1

## Slide 34: Example: Convert 105 decimal number in to it’s equivalent binary number.
2 | 105
2 | 52
2 | 26
2 | 13
2 | 6
2 | 3
2 | 1
 | 0
1
0
0
1
0
1
1

## Slide 35: Example: Convert 105 decimal number in to it’s equivalent binary number.
2 | 105
2 | 52
2 | 26
2 | 13
2 | 6
2 | 3
2 | 1
 | 0
1
0
0
1
0
1
1
LSB
MSB
(105)10  (1101001)2

## Slide 36: Procedure:
Multiply the given fractional number by base 2.
Record the carry generated in this multiplication as MSB.
Multiply only the fractional number of the product in step 2 by 2 and record the carry as the next bit to MSB.
Repeat the steps 2 and 3 up to 5 bits. The last carry will represent the LSB of equivalent binary number
Conversion of Decimal number into Binary number (Fractional Number)
36

## Slide 37: Example: Convert 0.42 decimal number in to it’s equivalent binary number.
37

## Slide 38: Example: Convert 0.42 decimal number in to it’s equivalent binary number.
0.42 X 2 = 0.84
0
38

## Slide 39: Example: Convert 0.42 decimal number in to it’s equivalent binary number.
0.42 X 2 | = | 0.84 | 0
0.84 X 2 | = | 1.68 | 1
39

## Slide 40: Example: Convert 0.42 decimal number in to it’s equivalent binary number.
0.42 X 2 | = | 0.84 | 0
0.84 X 2 | = | 1.68 | 1
0.68 X 2 | = | 1.36 | 1
40

## Slide 41: Example: Convert 0.42 decimal number in to it’s equivalent binary number.
0.42 X 2 | = | 0.84 | 0
0.84 X 2 | = | 1.68 | 1
0.68 X 2 | = | 1.36 | 1
0.36 X 2 | = | 0.72 | 0
41

## Slide 42: Example: Convert 0.42 decimal number in to it’s equivalent binary number.
0.42 X 2 | = | 0.84 | 0
0.84 X 2 | = | 1.68 | 1
0.68 X 2 | = | 1.36 | 1
0.36 X 2 | = | 0.72 | 0
0.72 X 2 | = | 1.44 | 1
42

## Slide 43: Example: Convert 0.42 decimal number in to it’s equivalent binary number.
0.42 X 2 | = | 0.84 | 0
0.84 X 2 | = | 1.68 | 1
0.68 X 2 | = | 1.36 | 1
0.36 X 2 | = | 0.72 | 0
0.72 X 2 | = | 1.44 | 1
MSB
(0.42)10  (0.01101)2
LSB
43

## Slide 44: Exercise
44
Convert following Decimal Numbers in to its equivalent Binary Number:
1. (1248.56)10 = ( ? )2
2. (8957.75)10 = ( ? )2
3. (420.6)10 = ( ? )2
4. (8476.47)10 = ( ? )2

## Slide 45: Conversion from Decimal Number to Octal Number
Hexadecimal
Decimal
Octal
Binary
45

## Slide 46: Conversion of Decimal Number into Octal Number (Integer Number)
Procedure:
Divide the decimal no by the base 8, noting the remainder.
Continue to divide the quotient by 8 until there is nothing left, keeping the track of the remainders from each step.
List the remainder values in reverse order to
8/29/2f0i1n7
d the number’s ocAmtitaNelvasee quivalent
60

## Slide 47: Example: Convert 204 decimal number in to it’s equivalent octal number.
47

## Slide 48
Example: Convert 204 decimal number in to it’s equivalent octal number.
8 204
48

## Slide 49: Example: Convert 204 decimal number in to it’s equivalent octal number.
8 | 204
8 | 25
4
8
2 5
204
- 16
44
- 40
4
49

## Slide 50: Example: Convert 204 decimal number in to it’s equivalent octal number.
8 | 204
8 | 25
8 | 3
4
1
8
3
25
- 24
1
50

## Slide 51: Example: Convert 204 decimal number in to it’s equivalent octal number.
8 | 204
8 | 25
8 | 3
 | 0
51
4
1
3

## Slide 52: Example: Convert 204 decimal number in to it’s equivalent octal number.
3
LSB
4
1
MSB
8 | 204
8 | 25
8 | 3
 | 0
52
(204)10  (314)8

## Slide 53: Procedure:
Multiply the given fractional number by base 8.
Record the carry generated in this multiplication as MSB.
Multiply only the fractional number of the product in step 2 by 8 and record the carry as the next bit to MSB.
Repeat the steps 2 and 3 up to 5 bits. The last carry will represent the LSB of equivalent octal number
Conversion of Decimal Number into Octal Number (Fractional Number)
53

## Slide 54: Example: Convert 0.6234 decimal number in to it’s equivalent Octal number.
54

## Slide 55: Example: Convert 0.6234 decimal number in to it’s equivalent Octal number.
0.6234 X 8 = 4.9872
4
55

## Slide 56: Example: Convert 0.6234 decimal number in to it’s equivalent Octal number.
0.6234 X 8 | = | 4.9872 | 4
0.9872 X 8 | = | 7.8976 | 7
56

## Slide 57: Example: Convert 0.6234 decimal number in to it’s equivalent Octal number.
0.6234 X 8 | = | 4.9872 | 4
0.9872 X 8 | = | 7.8976 | 7
0.8976 X 8 | = | 7.1808 | 7
57

## Slide 58: Example: Convert 0.6234 decimal number in to it’s equivalent Octal number.
0.6234 X 8 | = | 4.9872 | 4
0.9872 X 8 | = | 7.8976 | 7
0.8976 X 8 | = | 7.1808 | 7
0.1808 X 8 | = | 1.4464 | 1
58

## Slide 59: Example: Convert 0.6234 decimal number in to it’s equivalent Octal number.
0.6234 X 8 | = | 4.9872 | 4
0.9872 X 8 | = | 7.8976 | 7
0.8976 X 8 | = | 7.1808 | 7
0.1808 X 8 | = | 1.4464 | 1
0.4464 X 8 | = | 3.5712 | 3
59

## Slide 60: Example: Convert 0.6234 decimal number in to it’s equivalent Octal number.
0.6234 X 8 | = | 4.9872 | 4
0.9872 X 8 | = | 7.8976 | 7
0.8976 X 8 | = | 7.1808 | 7
0.1808 X 8 | = | 1.4464 | 1
0.4464 X 8 | = | 3.5712 | 3
MSB
(0.6234)10  (0.47713)8
LSB
60

## Slide 61: Exercise
61
Convert following Decimal Numbers in to its equivalent Octal Number:
1. (1248.56)10 = ( 2340.43656 )8
2. (8957.75)10 = ( 21375.6 )8
3. (420.6)10 = ( 644.463 1)8
4. (8476.47)10 = ( 20434.36 )8

## Slide 62: Conversion from Decimal Number to Hex Number
Hexadecimal
Decimal
Octal
Binary
62

## Slide 63: Conversion of Decimal Number into Hexadecimal Number (Integer Number)
Procedure:
Divide the decimal no by the base 16, noting the remainder.
Continue to divide the quotient by 16 until there is nothing left, keeping the track of the remainders from each step.
List the remainder values in reverse order to
8/29/2f0i1n7
d the number’s heAmxit Neevasqe uivalent
77

## Slide 64: Example: Convert 2003 decimal number in to it’s equivalent Hex number.
64

## Slide 65: Example: Convert 2003 decimal number in to it’s equivalent Hex number.
16 2003
65

## Slide 66: Example: Convert 2003 decimal number in to it’s equivalent Hex number.
16 | 2003
16 | 125
3
3
1 2 5
16 2003
- 16
40
- 32
83
- 80
3
66

## Slide 67: Example: Convert 2003 decimal number in to it’s equivalent Hex number.
16 | 2003
16 | 125
16 | 7
3
13
3
D
7
16 125
- 112
13
67

## Slide 68: Example: Convert 2003 decimal number in to it’s equivalent Hex number.
16 | 2003
16 | 125
16 | 7
 | 0
68
3
7
13
3
7
D

## Slide 69: Example: Convert 2003 decimal number in to it’s equivalent Hex number.
3
7
13
LSB
MSB
16 | 2003
16 | 125
16 | 7
 | 0
69
3
7
D
(2003)10  (7 D3)16

## Slide 70: Conversion of Decimal Number into Hexadecimal Number (Fractional Number)
Procedure:
Multiply the given fractional number by base 16.
Record the carry generated in this multiplication as MSB.
Multiply only the fractional number of the product in step 2 by 16 and record the carry as the next bit to MSB.
Repeat the steps 2 and 3 up to 5 bits. The last carry will represent the LSB of equivalent hex
number

## Slide 71: Example: Convert 0.122 decimal number in to it’s equivalent Hex number.
71

## Slide 72: Example: Convert 0.122 decimal number in to it’s equivalent Hex number.
0.122 X 16 = 1.952
1
1
72

## Slide 73: Example: Convert 0.122 decimal number in to it’s equivalent Hex number.
0.122 X 16 = 1.952
0.952 X 16 = 15.232
1
15
1
F
73

## Slide 74: Example: Convert 0.122 decimal number in to it’s equivalent Hex number.
0.122 X 16 | = | 1.952 | 1 | 1
0.952 X 16 | = | 15.232 | 15 | F
0.232 X 16 | = | 3.712 | 3 | 3
74

## Slide 75: Example: Convert 0.122 decimal number in to it’s equivalent Hex number.
0.122 X 16 | = | 1.952 | 1 | 1
0.952 X 16 | = | 15.232 | 15 | F
0.232 X 16 | = | 3.712 | 3 | 3
0.712 X 16 | = | 11.392 | 11 | B
75

## Slide 76: Example: Convert 0.122 decimal number in to it’s equivalent Hex number.
0.122 X 16 | = | 1.952 | 1 | 1
0.952 X 16 | = | 15.232 | 15 | F
0.232 X 16 | = | 3.712 | 3 | 3
0.712 X 16 | = | 11.392 | 11 | B
0.392 X 16 | = | 6.272 | 6 | 6
76

## Slide 77: Example: Convert 0.122 decimal number in to it’s equivalent Hex number.
0.122 X 16 = 1.952
1
0.952 X 16 | = | 15.232 | 15
0.232 X 16 | = | 3.712 | 3
0.712 X 16 | = | 11.392 | 11
0.392 X 16 | = | 6.272 | 6
1
F 3 B 6
MSB
LSB
(0.122)10  (0.1F3B6)16
77

## Slide 78: Exercise
78
Convert following Decimal Numbers in to its equivalent Hex Number:
1. (1248.56)10 = ( ? )16
2. (8957.75)10 = ( ? )16
3. (420.6)10 = ( ? )16
4. (8476.47)10 = ( ? )16

## Slide 79: Conversion from Binary Number to Decimal Number
Hexadecimal
Decimal
Octal
Binary
79

## Slide 80: Conversion of Binary Number into Decimal Number
Procedure:
Write down the binary number.
Write down the weights for different positions.
Multiply each bit in the binary number with the corresponding weight to obtain product numbers to get the decimal numbers.
Add all the product numbers to get the decimal
94

## Slide 81: Example: Convert 1011.01 binary number in to it’s equivalent decimal number.

## Slide 82: Example: Convert 1011.01 binary number in to it’s equivalent decimal number.
Binary No.
.
1
0 0
1 1 1

## Slide 83: Example: Convert 1011.01 binary number in to it’s equivalent decimal number.
Binary No.
Positional Weights
.
1
0 0
1 1 1
20
21
23 22
21 22

## Slide 84: Example: Convert 1011.01 binary number in to it’s equivalent decimal number.
Binary No.
Positional Weights
.
1
0 0
1 1 1
20
23 22 21 21 22
 (1 23 )  (0 22 )  (1 21 )  (1 20 ).(0 21)  (1 22 )

## Slide 85: Example: Convert 1011.01 binary number in to it’s equivalent decimal number.
Binary No.
Positional Weights
.
1
0 0
1 1 1
20
23 22 21 21 22
 (1 23 )  (0 22 )  (1 21 )  (1 20 ).(0 21)  (1 22 )
= 8 + 0 + 2 + 1 . 0 + 0.25

## Slide 86: Example: Convert 1011.01 binary number in to it’s equivalent decimal number.
Binary No.
Positional Weights
.
1
0 0
1 1 1
20
23 22 21 21 22
 (1 23 )  (0 22 )  (1 21 )  (1 20 ).(0 21)  (1 22 )
= 8 + 0 + 2 + 1 . 0 + 0.25
= 11.25

## Slide 87: Example: Convert 1011.01 binary number in to it’s equivalent decimal number.
Binary No.
Positional Weights
.
1
0 0
1 1 1
20
23 22 21 21 22
 (1 23 )  (0 22 )  (1 21 )  (1 20 ).(0 21)  (1 22 )
= 8 + 0 + 2 + 1 . 0 + 0.25
= 11.25
(1011.01)2  (11.25)10

## Slide 88: Exercise
Convert following Binary Numbers in to its equivalent Decimal Number:
1. (1101110.011)2 = ( ? )10
2. (1101.11)2 = ( ? )10
3. (10001.01)2 = ( ? )10

## Slide 89: Conversion from Octal Number to Decimal Number
Hexadecimal
Decimal
Octal
Binary

## Slide 90: Conversion of Octal Number into Decimal Number
Procedure:
Write down the octal number.
Write down the weights for different positions.
Multiply each bit in the binary number with the corresponding weight to obtain product numbers to get the decimal numbers.
Add all the product numbers to get the decimal
uivalent
104

## Slide 91: Example: Convert 365.24 octal number in to it’s equivalent decimal number.

## Slide 92: Example: Convert 365.24 octal number in to it’s equivalent decimal number.
Octal No.
.
2 4
3 6 5

## Slide 93: Example: Convert 365.24 octal number in to it’s equivalent decimal number.
Octal No.
Positional Weights
.
2 4
3 6 5
82 81 80
81 82

## Slide 94: Example: Convert 365.24 octal number in to it’s equivalent decimal number.
Octal No.
Positional Weights
.
2 4
3 6 5
82 81 80 81 82
 (382 )  (681 )  (580 ).(281)  (482 )

## Slide 95: Example: Convert 365.24 octal number in to it’s equivalent decimal number.
Octal No.
Positional Weights
.
2 4
3 6 5
82 81 80 81 82
 (382 )  (681 )  (580 ).(281)  (482 )
= 192 + 48 + 5 . 0.25 +0.0625

## Slide 96: Example: Convert 365.24 octal number in to it’s equivalent decimal number.
Octal No.
Positional Weights
.
2 4
110
3 6 5
82 81 80 81 82
 (382 )  (681 )  (580 ).(281)  (482 )
= 192 + 48 + 5 . 0.25 +0.0625
= 245.3125

## Slide 97: Example: Convert 365.24 octal number in to it’s equivalent decimal number.
Octal No.
Positional Weights
.
2 4
3 6 5
82 81 80 81 82
 (382 )  (681 )  (580 ).(281)  (482 )
= 192 + 48 + 5 . 0.25 +0.0625
= 245.3125
(365.24)8  (245.3125)10

## Slide 98: Exercise
Convert following Octal Numbers in to its equivalent Decimal Number:
1. (3006.05)8 = ( ? )10
2. (273.56)8 = ( ? )10
3. (6534.04)8 = ( ? )10

## Slide 99: Conversion from Hex Number to Decimal Number
Hexadecimal
Decimal
Octal
Binary

## Slide 100: Procedure:
Write down the hex number.
Write down the weights for different positions.
Multiply each bit in the binary number with the corresponding weight to obtain product
numbers to get the decimal numbers.
4. Add all the product numbers to
decimal equivalent
get the
114
Conversion of Hexadecimal Number into Decimal Number

## Slide 101: Example: Convert 5826 hex number in to it’s equivalent decimal number.

## Slide 102: Example: Convert 5826 hex number in to it’s equivalent decimal number.
Hex No.
5 8 6
2

## Slide 103: Example: Convert 5826 hex number in to it’s equivalent decimal number.
Hex No.
Positional Weights
5 8 6
2
161
163 162
160

## Slide 104: Example: Convert 5826 hex number in to it’s equivalent decimal number.
Hex No.
Positional Weights
5 8 6
2
163 162 161 160
 (5163 )  (8162 )  (2161 )  (6160 )

## Slide 105: Example: Convert 5826 hex number in to it’s equivalent decimal number.
Hex No.
Positional Weights
5 8 6
2
163 162 161 160
 (5163 )  (8162 )  (2161 )  (6160 )
=20480 + 2048 + 32 + 6

## Slide 106: Example: Convert 5826 hex number in to it’s equivalent decimal number.
Hex No.
Positional Weights
5 8 6
120
2
163 162 161 160
 (5163 )  (8162 )  (2161 )  (6160 )
=20480 + 2048 + 32 + 6
= 22566

## Slide 107: Example: Convert 5826 hex number in to it’s equivalent decimal number.
Hex No.
Positional Weights
5 8 6
2
163 162 161 160
 (5163 )  (8162 )  (2161 )  (6160 )
=20480 + 2048 + 32 + 6
= 22566
(5826)16  (22566)10

## Slide 108: Exercise
Convert following Hexadecimal Numbers in to its equivalent Decimal Number:
1. (4056)16 = ( ? )10
2. (6B7)16 = ( ? )10
3. (8E47.AB)16 = ( ? )10

## Slide 109: Conversion from Binary Number to Octal Number
Hexadecimal
Decimal
Octal
Binary

## Slide 110: Conversion of Binary Number into Octal Number
Procedure:
Group the binary bits into groups of 3 starting from LSB.
Convert each group into its equivalent decimal.
As the number of bits in each group is restricted to 3, the decimal number will be same as octal number

## Slide 111: Example: Convert 11010010 binary number in to it’s equivalent octal number.

## Slide 112
Example: Convert 11010010 binary
number in to it’s equivalent octal number.
0 1 1 0 1 0 0 1 0

## Slide 113: Example: Convert 11010010 binary number in to it’s equivalent octal number.
LSB
0 1 1 0 1 0 0 1 0

## Slide 114: Example: Convert 11010010 binary number in to it’s equivalent octal number.
0 1 1 0 1 0 0 1 0
3
2
2

## Slide 115: Example: Convert 11010010 binary number in to it’s equivalent octal number.
0 1 1 0 1 0 0 1 0
3
2
2
(11010010)2  (322)8

## Slide 116: Exercise
130
Convert following Binary Numbers in to its equivalent Octal Number:
1. (1101110.011)2 = ( ? )8
2. (1101.11)2 = ( ? )8
3. (10001.01)2 = ( ? )8

## Slide 117: Conversion from Binary Number to Hexadecimal Number
Hexadecimal
Decimal
Octal
Binary

## Slide 118: Conversion of Binary Number to Hexadecimal Number
Procedure:
Group the binary bits into groups of 4 starting from LSB.
Convert each group into its equivalent decimal.
As the number of bits in each group is restricted to 4, the decimal number will be same as hex number

## Slide 119: Example: Convert 11010010 binary number in to it’s equivalent hex number.

## Slide 120: Example: Convert 11010010 binary number in to it’s equivalent hex number.
LSB
1 1 0 1 0 0 1 0

## Slide 121: Example: Convert 11010010 binary number in to it’s equivalent hex number.
LSB
1 1 0 1 0 0 1 0

## Slide 122: Example: Convert 11010010 binary number in to it’s equivalent hex number.
1 1 0 1 0 0 1 0
D
2

## Slide 123: Example: Convert 11010010 binary number in to it’s equivalent hex number.
1 1 0 1 0 0 1 0
D
2
(11010010)2  (D2)16

## Slide 124: Exercise
Convert following Binary Numbers in to its equivalent Hexadecimal Number:
1. (1101110.011)2 = ( ? )16
2. (1101.11)2 = ( ? )16
3. (10001.01)2 = ( ? )16

## Slide 125: Conversion from Octal Number to Binary Number
Hexadecimal
Decimal
Octal
Binary

## Slide 126: Conversion of Octal Number into Binary Number
To get the binary equivalent of the given octal number we have to convert each octal digit into its equivalent 3 bit binary number
140

## Slide 127: Example: Convert 364 octal number in to it’s equivalent binary number.

## Slide 128: Example: Convert 364 octal number in to it’s equivalent binary number.
3
6
4

## Slide 129: Example: Convert 364 octal number in to it’s equivalent binary number.
3 | 6 | 4
011 | 110 | 100

## Slide 130: Example: Convert 364 octal number in to it’s equivalent binary number.
3 | 6 | 4
011 | 110 | 100
(364)8  (0111101100)2

## Slide 131: Example: Convert 364 octal number in to it’s equivalent binary number.
3 | 6 | 4
011 | 110 | 100
(364)8  (0111101100)2
OR
(364)8  (111101100)2

## Slide 132: Exercise
Convert following Octal Numbers in to its equivalent Binary Number:
1. (3006.05)8 = ( ? )2
2. (273.56)8 = ( ? )2
3. (6534.04)8 = ( ? )2

## Slide 133: Conversion from Hex Number to Binary Number
Hexadecimal
Decimal
Octal
Binary

## Slide 134: Conversion of Hexadecimal Number into Binary Number
To get the binary equivalent of the given hex number we have to convert each hex digit into its equivalent 4 bit binary number

## Slide 135: Example: Convert AFB2 hex number in to it’s equivalent binary number.

## Slide 136: Example: Convert AFB2 hex number in to it’s equivalent binary number.
A
150
F
B
2

## Slide 137: Example: Convert AFB2 hex number in to it’s equivalent binary number.
A
F
B
2
1010
1111
1011
0010

## Slide 138: Example: Convert AFB2 hex number in to it’s equivalent binary number.
A
F
B
2
1010
1111
1011
0010
(AFB2)16  (1010111110110010)2

## Slide 139: Exercise
Convert following Hexadecimal Numbers in to its equivalent Binary Number:
1. (4056)16 = ( ? )2
2. (6B7)16 = ( ? )2
3. (8E47.AB)16 = ( ? )2

## Slide 140: Conversion from Octal Number to Hex Number
Hexadecimal
Decimal
Octal
Binary

## Slide 141: Conversion of Octal Number into Hexadecimal Number
To get hex equivalent number of given octal number, first we have to convert octal number into its 3 bit binary equivalent and then convert binary number into its hex equivalent.

## Slide 142: Example: Convert 364 octal number in to it’s equivalent hex number.

## Slide 143: Example: Convert 364 octal number in to it’s equivalent hex number.
3
6
4
Octal Number

## Slide 144: Example: Convert 364 octal number in to it’s equivalent hex number.
3 | 6 | 4 | Octal Number
011 | 110 | 100 | Binary Number

## Slide 145: Example: Convert 364 octal number in to it’s equivalent hex number.
3 | 6 | 4 | Octal Number
011 | 110 | 100 | Binary Number
 | 011110100 |  | Binary Number

## Slide 146: Example: Convert 364 octal number in to it’s equivalent hex number.
3 |  | 6 | 4 | Octal Number
011 |  | 110 | 100 | Binary Number
 |  | 011110100 |  | Binary Number
 | 0 | F 4 |  | Hex Number
160

## Slide 147: Example: Convert 364 octal number in to it’s equivalent hex number.
3 |  | 6 | 4 | Octal Number
011 |  | 110 | 100 | Binary Number
 |  | 011110100 |  | Binary Number
 | 0 | F 4 |  | Hex Number
(364)8  (F4)16

## Slide 148: Exercise
Convert following Octal Numbers in to its equivalent Hex Number:
1. (3006.05)8 = ( ? )16
2. (273.56)8 = ( ? )16
3. (6534.04)8 = ( ? )16

## Slide 149: Conversion from Hex Number to Octal Number
Hexadecimal
Decimal
Octal
Binary

## Slide 150: Conversion of Hexadecimal Number into Octal Number
To get octal equivalent number of given hex number, first we have to convert hex number
into its 4 bit binary equivalent convert binary number into
and then its octal
equivalent.

## Slide 151: Example: Convert 4CA hex number in to it’s equivalent octal number.

## Slide 152: Example: Convert 4CA hex number in to it’s equivalent octal number.
4
C
A
Hex Number

## Slide 153: Example: Convert 4CA hex number in to it’s equivalent octal number.
4
C
A
Hex Number
0100
1100
1010
Binary Number

## Slide 154: Example: Convert 4CA hex number in to it’s equivalent octal number.
4
C
A
Hex Number
0100
1100
1010
Binary Number
010011001010
Binary Number

## Slide 155: Example: Convert 4CA hex number in to it’s equivalent octal number.
4
C
A
Hex Number
0100
1100
1010
Binary Number
010011001010
Binary Number
2 3 1 2
Octal Number

## Slide 156: Example: Convert 4CA hex number in to it’s equivalent octal number.
4
C
A
Hex Number
0100
1100
1010
Binary Number
010011001010
Binary Number
Octal Number
2 3 1 2
(4CA)16  (2312)8
170

## Slide 157: Exercise
Convert following Hexadecimal Numbers in to its equivalent Octal Number:
1. (4056)16 = ( ? )8
2. (6B7)16 = ( ? )8
3. (8E47.AB)16 = ( ? )8

## Slide 158: Chapter I – Number System
Introduction to digital signal, Advantages of Digital System over analog systems)Number Systems: Different types of number systems( Binary, Octal, Hexadecimal ), Conversion of number systems,
  Binary arithmetic: Addition, Subtraction, Multiplication, Division.
  Subtraction using 1’s complement and 2’s complement
Codes
  Codes -BCD, Gray Code, Excess-3, ASCII code
  BCD addition, BCD subtraction using 9’s and 10’ complement
(Numericals based on above topic).

## Slide 159: Binary Addition
Following are the four most basic cases for binary addition
0 | + | 0 | = | 0
0 | + | 1 | = | 1
1 | + | 0 | = | 1
1 | + | 1 | = | 10 i.e. 0 with carry 1

## Slide 160
Binary Addition
Example: Perform (10111)2  (11001)2

## Slide 161: Binary Addition
 |  |  | 1 | 
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
0
Example: Perform (10111)2  (11001)2

## Slide 162: Binary Addition
 |  |  |  |  | 1 | 1 | 
 |  |  | 1 | 0 | 1 | 1 | 1
 |  |  | 1 | 1 | 0 | 0 | 1
 |  |  |  |  |  | 0 | 0
Example: Perform (10111)2  (11001)2

## Slide 163: Binary Addition
 |  |  |  | 1 | 1 |  | 
 |  |  | 1 | 0 | 1 | 1 | 1
 |  |  | 1 | 1 | 0 | 0 | 1
 |  |  |  |  | 0 | 0 | 0
Example: Perform (10111)2  (11001)2

## Slide 164: Binary Addition
 |  |  | 1 | 1 |  |  | 
 |  |  | 1 | 0 | 1 | 1 | 1
 |  |  | 1 | 1 | 0 | 0 | 1
 |  |  |  | 0 | 0 | 0 | 0
Example: Perform (10111)2  (11001)2

## Slide 165: Binary Addition
Example: Perform (10111)2  (11001)2
1
1 0 1 1 1
1 1 0 0 1
1 1 0 0 0 0

## Slide 166: Binary Addition
Example: Perform (10111)2  (11001)2
1 1 1 1
1 0 1 1 1
1 1 0 0 1
1 1 0 0 0 0
(10111)2  (11001)2  (110000)2
180

## Slide 167
Binary Addition
Example: Perform (1101.101)2  (111.011)2

## Slide 168: Binary Addition
 |  |  |  | 1 | 1 | 1 | 1 | 1 1 | 
 |  |  |  | 1 | 1 | 0 | 1 . | 1 0 | 1
 |  |  |  |  | 1 | 1 | 1 . | 0 1 | 1
 |  |  | 1 | 0 | 1 | 0 | 1 . | 0 0 | 0
Example: Perform (1101.101)2  (111.011)2
(1101.101)2  (111.011)2  (10101.000)2

## Slide 169: Exercise
Perform Binary Addition of following:
1. (11011)2+(1101)2 =101000
2. (1011)2+(1101)2+(1001)2+(1111)2 =110000
3. (1010.11)2+(1101.10)2+(1001.11)2+(1111.11)2
=110001.11
4. (10111.101)2+(110111.01)2 =101110.110

## Slide 170: Binary Subtraction
Following are the four most basic cases for binary subtraction
 |  |  | Subtraction | Borrow
0 | - | 0 | = 0 | 0
0 | - | 1 | = 1 | 1
1 | - | 0 | = 1 | 0
1 | - | 1 | = 0 | 0

## Slide 171
Binary Subtraction
Example: Perform (1010.010)2  (111.111)2

## Slide 172: Binary Subtraction
 | 1 |  | 1 | 1 | 10 | 
0 | 10 | 0 | 10 | 10 | 0 | 10
1 | 0 | 1 | 0 . | 0 | 1 | 0
 | 1 | 1 | 1 . | 1 | 1 | 1
0 | 0 | 1 | 0 . | 0 | 1 | 1
Example: Perform (1010.010)2  (111.111)2
(1010.010)2  (111.111)2  (0010.011)2

## Slide 173: Exercise
Perform Binary Subtraction of following:
1. (1011)2- (101)2
2. (1100.10)2- (111.01)2
3. (10110)2- (1011)2
4. (10001.01)2- (1111.11)2

## Slide 174: Binary Multiplication
Following are the four most basic cases for binary multiplication
0 | X | 0 | = | 0
0 | X | 1 | = | 0
1 | X | 0 | = | 0
1 | X | 1 | = | 1

## Slide 175: Binary Multiplication
Example: Perform
(1001)2  (1000)2

## Slide 176: Binary Multiplication
Example: Perform
 |  |  |  |  |  |  | 1 | 0 | 0 | 1
 |  |  |  |  |  |  | 1 | 0 | 0 | 0
 |  |  |  |  |  |  | 0 | 0 | 0 | 0
 |  |  |  |  |  | 0 | 0 | 0 | 0 | x
 |  |  |  |  | 0 | 0 | 0 | 0 | x | x
 |  |  |  | 1 | 0 | 0 | 1 | x | x | x
 |  |  |  | 1 | 0 | 0 | 1 | 0 | 0 | 0
(1001)2  (1000)2
190
(1001)2  (1000)2  (1001000)2

## Slide 177: Exercise
Perform Binary Multiplication of following:
1. (1101)2 X (101)2
2. (1101.11)2 X (101.1)2
3. (11001)2 X (10)2
4. (10110)2 X (10.1)2

## Slide 178: Binary Division
Example: Perform
(110110)2 / (101)2

## Slide 179: Binary Division
8/29/2017
193
Example: Perform
1 | 0 | 1 | 0 |  |  | 
1 | 1 | 0 | 1 | 1 | 0 | 
-1 | 0 | 1 |  |  |  | 
0 | 0 | 1 | 1 |  |  | 
 |  | -0 | 0 |  |  | 
 |  | 1 | 1 | 1 |  | 
 |  | -1 | 0 | 1 |  | 
 |  | 0 | 1 | 0 | 0 | 
 |  |  | -0 | 0 | 0 | 
101
1 0 0Amit Nevase
(110110)2 / (101)2

## Slide 180: Exercise
Perform Binary Division of following:
1. (1010)2 by (11)2
2. (11110)2 by (101)2
3. (11011)2 by (10.1)2
4. (110111.1)2 by (101)2

## Slide 181: Chapter I – Number System
Introduction to digital signal, Advantages of Digital System over analog systems
  Number Systems: Different types of number systems( Binary, Octal, Hexadecimal ), Conversion of number systems,
  Binary arithmetic: Addition, Subtraction, Multiplication, Division.
using 1’s complement and 2’s
Subtraction complement
Codes
  Codes -BCD, Gray Code, Excess-3, ASCII code
  BCD addition, BCD subtraction using 9’s and 10’ complement
(Numericals based on above topic).

## Slide 182
1’s Complement
The 1’s complement of a number is obtained by simply complementing each bit of the number that is by changing all 0’s to 1’s and all 1’s to 0’s.
This system is called as 1’s complement because the number can be subtracted from 1 to obtain result

## Slide 183: 1’s Complement
Example: Obtain 1’s complement of the 1010
1 | 1 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 0 | 1
1’s complement of the 1010 is 0101

## Slide 184: 1’s Complement
8/29/2017
Amit Nevase
198
Sr. No. | Binary Number | 1’s Complement
1 | 1101 0101 | 0010 1010
2 | 1001 | 0110
3 | 1011 1111 | 0100 0000
4 | 1101 1010 0001 | 0010 0101 1110
5 | 1110 0111 0101 | 0001 1000 1010
6 | 1011 0100 1001 | 0100 1011 0110
7 | 1100 0011 0010 | 0011 1100 1101
8 | 0001 0010 1000 | 1110 1101 0111

## Slide 185
Subtraction Using 1’s Complement
In 1’s complement subtraction, add the 1’s complement of subtrahend to the minuend.
If there is carry out, bring the carry around and add it to LSB.
Look at the sing bit (MSB), if this is 0, the result is positive and is in its true binary form.
If the MSB is 1(whether there is a carry or no carry at all), the result is negative & is in its 1’s complement form. So take 1’s complement to obtain result.

## Slide 186: Subtraction using 1’s Complement
Example: Perform using 1’ complement
(9)10  (4)10

## Slide 187: Subtraction using 1’s Complement
Example: Perform using 1’ complement
Step 1: Take 1’ complement of
1 0 0 1
1 0 1 1
Step 3:If carry is generated add final carry to the result
final carry
1 0 1 0 0
Result
(9)10  (4)10
(4)10  (0100)2
 1011
Step 2: Add 9 with 1’ complement of 4

## Slide 188: Example
Continue
1 0 0 1
1 0 1 1
1 0 1 0 0
1
0 1 0 1
When the final carry is produced the answer is positive and is in its true binary form
final carry
Result
Final Result

## Slide 189
Exercise
using 1’s
Perform Binary Subtraction Complement method
1. (52)10 - (17)10
2. (46)10 - (84)10
3. (63.75)10-(17.5)10
4. (73.5)10-(112.75)10

## Slide 190: 2’s Complement
The 2’s complement of a number is obtained by adding 1 to the 1’s complement of that number

## Slide 191
2’s Complement
Example: Obtain 2’s complement of the 1010

## Slide 192: 2’s Complement
Example: Obtain 2’s complement of the 1010
1 | 1 | 1 | 1 | 
1 | 0 | 1 | 0 | 
0 | 1 | 0 | 1 | ---1’s complement
 |  |  | 1 | 
0 | 1 | 1 | 0 | ----2’s complement
2’s complement of the 1010 is 0110

## Slide 193: 2’s Complement
Sr. No. | Binary Number | 1’s Complement | 2’s Complement
1 | 1101 0101 | 0010 1010 | 0010 1011
2 | 1001 | 0110 | 0111
3 | 1011 1111 | 0100 0000 | 0100 0001
4 | 1101 1010 0001 | 0010 0101 1110 | 0010 0101 1111
5 | 1110 0111 0101 | 0001 1000 1010 | 0001 1000 1011

## Slide 194: Subtraction Using 2’s Complement
In 2’s complement subtraction, add the 2’s complement of subtrahend to the minuend.
If carry is generated then the result is positive and in its true form.
If the carry is not produced, then the result is negative and in its 2’s complement form.
*Carry is always to be discarded

## Slide 195: Subtraction Using 2’s Complement
Example: Perform using 2’ complement
(9)10  (4)10

## Slide 196: Subtraction Using 2’s Complement
210
Example: Perform using 2’ complement
Step 1: Take 2’ complement of
1 0 0 1
1 1 0 0
If Carry is generated, discard carry. The result is positive and its true
bin8/a29r/y201f7orm
final carry
Discard
1 0 1 0 1
Final Result
(9)10  (4)10
(4)10  (0100)2
 10111  1100
Step 2: Add 9 with 2’ complement of 4

## Slide 197
Exercise
using 2’s
Perform Binary Subtraction Complement method
1. (46)10 - (19)10
2. (27)10 - (75)10
3. (125.3)10-(46.7)10
4. (36.75)10-(89.5)10

## Slide 198: Chapter I – Number System
Introduction to digital signal, Advantages of Digital System over analog systems
  Number Systems: Different types of number systems( Binary, Octal, Hexadecimal ), Conversion of number systems,
  Binary arithmetic: Addition, Subtraction, Multiplication, Division.
  Subtraction using 1’s complement and 2’s complement
Codes
  Codes -BCD, Gray Code, Excess-3, ASCII code
  BCD addition, BCD subtraction using 9’s and 10’ complement
(Numericals based on above topic).

## Slide 199
BCD or 8421 Code
The smallest BCD number is (0000) and the largest is (1001). The next number to 9 will be 10 which is expressed as (0001 0000) in BCD.
There are six illegal combinations 1010, 1011, 1100, 1101, 1110 and 1111 in this code i.e. they are not part of the 8421 BCD code

## Slide 200: Decimal to BCD Conversion
Sr. No. | Decimal Number | BCD Code
1 | 8 | 1000
2 | 47 | 0100 0111
3 | 345 | 0011 0100 0101
4 | 99 | 1001 1001
5 | 10 | 0001 0000

## Slide 201
Exercise
Convert following Decimal Numbers into BCD 1. (286)10
2. (807)10
3. (429.5)10
4. (158.7)10

## Slide 202: Chapter I – Number System
Introduction to digital signal, Advantages of Digital System over analog systems
  Number Systems: Different types of number systems( Binary, Octal, Hexadecimal ), Conversion of number systems,
  Binary arithmetic: Addition, Subtraction, Multiplication, Division.
  Subtraction using 1’s complement and 2’s complement
Codes
  Codes -BCD, Gray Code, Excess-3, ASCII code
  BCD addition, BCD subtraction using 9’s and 10’ complement
(Numericals based on above topic).

## Slide 203
BCD Addition
The BCD addition is performed by individually adding the corresponding digits of the decimal number expressed in 4 bit binary groups starting from LSB.
If there is no carry & the sum term is not an illegal code, no correction is needed.

## Slide 204
BCD Addition
If there is a carry out of one group to the next group or if the sum term is an illegal code then 6
i.e. 0110 is added to the sum term of that group and resulting carry is added to the next group.
This is done to skip the six illegal states.

## Slide 205: BCD Addition
Addition of two BCD numbers
Sum≤9, Carry=0
Sum≤9, Carry=1
Sum>9, Carry=0
Answer is correct. No correction required.
Add 6 to the sum term to get the correct answer
Add 6 to the sum term to get the correct answer

## Slide 206
BCD Addition
Example: Perform in BCD (57)10  (26)10
220

## Slide 207: BCD Addition
57
26
0 1 0 1 0 1 1 1
0 0 1 0 0 1 1 0
83
0 0 1 1 1 1 1 0 1
Valid BCD Invalid BCD
Code Code
Final Carry 0
Thus we have to add 0110 in illegal BCD code
Example: Perform in BCD (57)10  (26)10

## Slide 208: Example
Continue
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Add 0110 in only invalid code
(57)10  (26)10  (83)10

## Slide 209
Exercise
Perform BCD Addition 1. (275)10 +(493)10 2. (109)10 +(778)10
3. (88.7)10 +(265.8)10
4. (204.6)10 +(185.56)10

## Slide 210: BCD Subtraction
The BCD subtraction is performed by subtracting the digits of each 4 bit group of the subtrahend from the corresponding 4 bit group of the minuend in binary starting from the LSD.

## Slide 211
BCD Subtraction
If there is no borrow from the next higher group then no correction is required .
If there is a borrow from the next group, then 0110 is subtracted from the difference term of this group.

## Slide 212: BCD Subtraction
Example: Perform in BCD
(38)10  (15)10

## Slide 213: BCD Subtraction
38 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0
15 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
23 0 0 0 1 0 0 0 1 1
Final Borrow 0 Valid BCD Valid BCD
Code Code
No borrow, hence difference is correct
Example: Perform in BCD (38)10  (15)10

## Slide 214
Exercise
Perform BCD Subtraction 1. (920)10 - (356)10
2. (79)10 - (27)10
3. (476.7)10 - (258.9)10
4. (634.6)10 - (328.7)10

## Slide 215: 9’s Complement
The nine’s complement of a BCD number can be obtained by subtracting each digit of BCD from 9.
Ex. Nine’s complement of 168
9
1
9 9
6 8
8 3 1
9’s complement of 168 is 831

## Slide 216: BCD Subtraction using 9’sComplement
Obtain 9’s complement of subtrahend
Add minuend with 9’s complement of subtrahend
If a carry is generated then add it to the sum to obtain the final result.
If a carry is not produced then the result is negative hence take the 9’s complement of the
8/2r9/e201s7 ult.
Amit Nevase
230

## Slide 217: BCD Subtraction using 9’s Complement
8/29/2017
Amit Nevase
231
Example: Perform in BCD using 9’s complement
(83)10  (21)10

## Slide 218: BCD Subtraction using 9’s Complement
232
Example: Perform in BCD using 9’s complement
9’s complement of 21 99-21=78
Add 83 with 9’s complement of 21 i.e. 78
83
78
1 0 0 0 0 0 1 1
0 1 1 1 1 0 0 0
1 1 1 1 1 0 1 1
Invalid BCD Invalid BCD Code Code
8/2T9/h201u7 s we have to add 0110AmiitnNevialsleegal BCD code
(83)10  (21)10

## Slide 219
Example:
continue……….
 |  |  | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
 |  |  | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
 |  |  |  |  |  | 1 |  |  |  | 
0 1 1 0
0 0 1
1 0 1 1 0 1 0 0 0 1
1
0
(83)10  (21)10  (62)10

## Slide 220
Exercise
Perform BCD Subtraction using 9’s Complement 1. (274)10 - (86)10
2. (93)10 - (615)10
3. (574.6)10 - (279.7)10
4. (376.3)10 - (765.6)10

## Slide 221: 10’s Complement
The 10’s complement of a BCD number can be obtained by adding 1 in 9’s complement.
Ex. 10’s complement of 168 9 9 9
1 6 8
8 3 1
1
8 3 2
10’s complement of 168 is 832

## Slide 222: BCD Subtraction using 10’s Complement
Obtain 10’s complement of subtrahend
Add minuend with 10’s complement of subtrahend
If a carry is generated, discard carry and result is positive and in its true form.
If a carry is not produced then the result is negative hence take the 10’s complement of the
8/2r9/e201s7 ult.
Amit Nevase
236

## Slide 223
8/29/2017
Amit Nevase
237
BCD Subtraction using 10’s Complement
Example: Perform in BCD using 10’s complement (83)10  (21)10

## Slide 224: BCD Subtraction using 10’s Complement
238
Add 83 with 10’s complement of 21 i.e. 79
83
79
1 0 0 0 0 0 1 1
0 1 1 1 1 0 0 1
1 1 1 1 1 1 0 0
Invalid BCD Invalid BCD Code Code
8/29/2T01h7 us we have to add 01A1m0it Neivnaseillegal BCD code
9’s complement of 21 10’s complement of 21
99-21=78
78+1=79
Example: Perform in BCD using 10’s complement (83)10  (21)10

## Slide 225: Example:
continue…….
 |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
 |  |  | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
 |  |  |  |  |  | 1 |  |  |  | 
1 0 1 1 0 1 0 0 1 0
0 1 1 0
0 0 1 0
(83)10  (21)10  (62)10
239

## Slide 226
Exercise
249
using
10’s
Perform BCD Subtraction Complement
1. (274)10 - (86)10
2. (93)10 - (615)10
3. (574.6)10 - (279.7)10
4. (376.3)10 - (765.6)10

## Slide 227: Chapter I – Number System
Introduction to digital signal, Advantages of Digital System over analog systems
  Number Systems: Different types of number systems( Binary, Octal, Hexadecimal ), Conversion of number systems,
  Binary arithmetic: Addition, Subtraction, Multiplication, Division.
  Subtraction using 1’s complement and 2’s complement
Codes
  Codes -BCD, Gray Code, Excess-3, ASCII code
  BCD addition, BCD subtraction using 9’s and 10’ complement
(Numericals based on above topic).

## Slide 228: Gray Code
The gray code is non-weighted code.
It is not suitable for arithmetic operations.
It is a cyclic code because successive code words in this code differ in one bit position only i.e. unit distance code

## Slide 229: Binary to Gray Code Conversion
If an n bit binary number is represented by
and its gray code equivalent by
where and are the MSBs,
then gray code bits are obtained from the binary code as follows;
…………
*where the symbol
represents Exclusive-OR operation
Bn, Bn  1,.......B1
Gn,Gn  1,.......G1

## Slide 230
Binary to Gray Code Conversion
Example 1: Convert 1011 Binary Number into Gray Code

## Slide 231: Binary to Gray Code Conversion
Example 1: Convert 1011 Binary Number into Gray Code
Binary Number
1
0
1
1

## Slide 232: Continue
Binary Number
1
0
1
1
Gray Code
1
Example 1:

## Slide 233: Example 1:
Continue
Binary Number
1
0
1
1
Gray Code
1
1


## Slide 234: Example 1:
Binary Number
1
0
1
1
Gray Code
1
1
1
Continue


## Slide 235: Example 1:
Binary Number
1
0
1
1
Gray Code
1
1
1
0
Continue


## Slide 236: Example 1:
Binary Number
1
1
Gray Code
1
1
1
0
250
Continue
1  0



## Slide 237
Binary to Gray Code Conversion
Example 2: Convert 1001 Binary Number into Gray Code

## Slide 238: Binary to Gray Code Conversion
Example 2: Convert 1001 Binary Number into Gray Code
Binary Number
1
0
0
1
Gray Code
1
1
0
1




## Slide 239
Binary to Gray Code Conversion
Example 3: Convert 1111 Binary Number into Gray Code

## Slide 240: Binary to Gray Code Conversion
Example 3: Convert 1111 Binary Number into Gray Code
Binary Number
1
1
1
1
Gray Code
1
0
0
0




## Slide 241
Binary to Gray Code Conversion
Example 4: Convert 1010 Binary Number into Gray Code

## Slide 242: Binary to Gray Code Conversion
Example 4: Convert 1010 Binary Number into Gray Code
Binary Number
0
0
Gray Code
1
1
1
1
1 

1 

## Slide 243: Binary and Corresponding Gray Codes
8/29/2017
Amit Nevase
257
Decimal No. | Binary No. | Gray Code
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0011
3 | 0011 | 0010
4 | 0100 | 0110
5 | 0101 | 0111
6 | 0110 | 0101
7 | 0111 | 0100
8 | 1000 | 1100
9 | 1001 | 1101
10 | 1010 | 1111
11 | 1011 | 1110
12 | 1100 | 1010
13 | 1101 | 1011
14 | 1110 | 1001
15 | 1111 | 1000

## Slide 244
Exercise
Binary
Numbers
into
Gray
Convert following Code
1. (1011)2
2. (110110010)2
3. (101010110101)2
4. (100001)2

## Slide 245: Gray Code to Binary Conversion
If an n bit gray code is represented by
and its binary equivalent then binary bits are obtained
from gray bits as follows;
Bn  Gn | Bn  1  Bn  Gn  1 | Bn  2  Bn  1  Gn  | 2 ………… | B1  B2  G1
*where the symbol
represents Exclusive-OR operation
Gn,Gn  1,.......G1
Bn, Bn  1,.......B1

## Slide 246
Gray Code to Binary Conversion
Example 1: Convert 1110 Gray code into Binary Number.
260

## Slide 247: Gray Code to Binary Conversion
Example 1: Convert 1110 Gray code into Binary Number.
Gray Code
1
1
1
0

## Slide 248: Continue
Example 1:
Gray Code
1
1
1
0
Binary Number
1

## Slide 249: Example 1:
Gray Code
1
1
1
0
Binary Number
1
0
Continue


## Slide 250: Example 1:
Gray Code
1
1
1
0
Binary Number
1
0
1
Continue


## Slide 251: Example 1:
Gray Code
1
1
1
0
Binary Number
1
0
1
1
Continue


## Slide 252: Example 1:
Gray Code
1
1
1
0
Binary Number
1
0
1
1
Continue




## Slide 253
Gray Code to Binary Conversion
Example 2: Convert 1101 Gray code into Binary Number.

## Slide 254: Gray Code to Binary Conversion
Example 2: Convert 1101 Gray code into Binary Number.
Gray Code
1
1
0
1
Binary Number
1
0
0
1




## Slide 255
Gray Code to Binary Conversion
Example 3: Convert 1100 Gray code into Binary Number.

## Slide 256: Gray Code to Binary Conversion
Example 3: Convert 1100 Gray code into Binary Number.
Gray Code
1
1
0
0
Binary Number
1
0
0
0

270



## Slide 257
Exercise
Gray Numbers into Binary
Convert following Numbers
1. (1111)GRAY
2. (101110) GRAY
3. (100010110) GRAY
4. (11100111) GRAY

## Slide 258: Excess-3 Code (XS-3)
The Xs-3 is non-weighted BCD code.
This code derives its name from the fact that each binary code word is the corresponding 8421 code word plus 0011.
It is a sequential code & therefore can be used for arithmetic operations.
It is a self complementing code

## Slide 259: Excess-3 Code (XS-3)
Decimal No. | BCD Code | Excess-3 Code= BCD + Excess-3
0 | 0000 | 0011
1 | 0001 | 0100
2 | 0010 | 0101
3 | 0011 | 0110
4 | 0100 | 0111
5 | 0101 | 1000
6 | 0110 | 1001
7 | 0111 | 1010
8 | 1000 | 1011
9 | 1001 | 1100

## Slide 260
Excess-3 Code (XS-3)
Example 1: Obtain Xs-3 Code for 428 Decimal

## Slide 261: Excess-3 Code (XS-3)
Example 1: Obtain Xs-3 Code for 428 Decimal
 | 4 | 2 | 8
 | 0100 | 0010 | 1000
+ | 0011 | 0011 | 0011
 | 0111 | 0101 | 1011

## Slide 262
Exercise
Convert following Decimal Numbers into Excess- 3 Code
1. (40)10
2. (88) 10
3. (64) 10
4. (23) 10

## Slide 263
ASCII Codes
The American Standard Code for Information Interchange is a character-encoding scheme originally based on the English alphabet.
ASCII codes represent text in computers, communications equipment, and other devices that use text.
Most modern character-encoding schemes are based on ASCII, though they support many additional characters.

## Slide 264
ASCII Codes
ASCII developed from telegraphic codes. Its first commercial use was as a seven-bit tele-printer code promoted by Bell data services.
Work on the ASCII standard began on October 6, 1960, with the first meeting of the American Standards Association's (ASA) X3.2 subcommittee.
The first edition of the standard was published during 1963.

## Slide 265
ASCII Codes
ASCII includes definitions for 128 characters: 33 are non-printing control characters (many now obsolete) that affect how text and space is processed and 95 printable characters, including the space (which is considered an invisible graphic)

## Slide 266: ASCII Codes
8/2
9/2017
A
mit Nevas
e
280
 |  |  |  | B7 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
 |  |  |  | B6 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
 |  |  |  | B5 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
B4 | B3 | B2 | B1 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | NUL | DLE | SP | 0 | @ | P | ‘ | p
0 | 0 | 0 | 1 | 1 | SOH | DC1 | ¦ | 1 | A | Q | a | q
0 | 0 | 1 | 0 | 2 | STX | DC2 | “ | 2 | B | R | b | r
0 | 0 | 1 | 1 | 3 | ETX | DC3 | # | 3 | C | S | c | s
0 | 1 | 0 | 0 | 4 | EOT | DC4 | $ | 4 | D | T | d | t
0 | 1 | 0 | 1 | 5 | ENQ | NAK | % | 5 | E | U | e | u
0 | 1 | 1 | 0 | 6 | ACK | SYN | & | 6 | F | V | f | v
0 | 1 | 1 | 1 | 7 | BEL | ETB | ‘ | 7 | G | W | g | w
1 | 0 | 0 | 0 | 8 | BS | CAN | ( | 8 | H | X | h | x
1 | 0 | 0 | 1 | 9 | HT | EM | ) | 9 | I | Y | i | y
1 | 0 | 1 | 0 | 10 | LF | SUB | “ | : | J | Z | j | z
1 | 0 | 1 | 1 | 11 | VT | ESC | + | ; | K | [ | k | {
1 | 1 | 0 | 0 | 12 | FF | FC | , | < | L | \ | l | !
1 | 1 | 0 | 1 | 13 | CR | GS |  | = | M | ] | m | }
1 | 1 | 1 | 0 | 14 | SO | RS | . | > | N | ^ | n | ~

## Slide 267: Online Tutorials
http://nptel.ac.in/video. php?subjectId=1171060 86
http://www.electronics- tutorials.ws/binary/bin_ 1.html

## Slide 268: Thank You
8/29/2017
283